## Slide 1: Lecture 15 Persistence More Hardware: RAID

## Slide 2: Seek, Rotate, Transfer
Must accelerate, coast, decelerate, settle
Seeks often take several milliseconds!
Settling alone can take 0.5 - 2 ms.
Entire seek often takes 4 - 10 ms.

## Slide 3: Seek, Rotate, Transfer
Depends on rotations per minute (RPM).
  7200 RPM is common, 15000 RPM is high end.
1 / 7200 RPM = 1 minute / 7200 rotations = 1 second / 120 rotations = 8.3 ms / rotation
so it may take 4.2 ms on avg to rotate to target (0.5 * 8.3 ms)

## Slide 4: Seek, Rotate, Transfer
Pretty fast — depends on RPM and sector density.
100+ MB/s is typical.
1s / 100 MB = 10 ms / MB = 4.9 us / sector (assuming 512-byte sector)

## Slide 5: Workload
So…
  seeks are slow
  rotations are slow
  transfers are fast
What kind of workload is fastest for disks?
  Sequential: access sectors in order (transfer dominated)
  Random: access sectors arbitrarily (seek+rotation dominated)

## Slide 6: Only One Disk?
Sometimes we want many disks — why?
  capacity
  performance
  reliability
Challenge: most file systems work on only one disk.

## Slide 7
“A Case for Redundant Arrays of Inexpensive Disks”, Patterson, et al.

## Slide 8: Solution 1: JBOD
JBOD: Just a Bunch Of Disks
Application is smart, stores different files on different file systems.
FS
FS
FS
FS
Application

## Slide 9: Solution 2: RAID
RAID: Redundant Array of Inexpensive Disks
  Transparent and deployable
  Capacity and performance
  Reliability?
FS
RAID Disk Controller
Application

## Slide 10: Why Inexpensive Disks?
Economies of scale! Cheap disks are popular.
  You can often get many commodity H/W components for the same price as a few expensive components.
Strategy: write S/W to build high-quality logical devices from many cheap devices.
Alternative to RAID: buy an expensive, high-end disk.

## Slide 11: General Strategy
Build fast, large disk from smaller ones.
Add even more disks for reliability.
Disk
RAID
0 100 200
Disk
Disk
Disk
0 100 0 100
0 100 0 100

## Slide 12: Redundancy
Redundancy: how many copies?
System engineers are always trying to increase or decrease redundancy.
  Increase: replication (e.g., RAID)
  Decrease: deduplication (e.g., code sharing)
One strategy: reduce redundancy as much is possible. Then add back just the right amount.

## Slide 14: Reasoning About RAID
Workload: types of reads/writes issued by app
  Reads and writes
  One operation and steady I/O
  Sequential and random
RAID: system for mapping logical to physical addrs
  Which logical blocks map to which physical blocks?
  How do we use extra physical blocks (if any)?
Metrics
  Capacity: how much space can apps use?
  Reliability: how many disks can we safely lose?
  Performance: how long does each workload take?

## Slide 15: RAID-0: Striping
Optimize for capacity.
No redundancy (weird name).
Logical Blocks
Disk 0 Disk 1

## Slide 16: RAID-0 with 4 disks
Disk 0 Disk 1 Disk 2 Disk 3
0 1 2 3
4 5 6 7
8 9 10 11
12 13 14 15
stripe
How to map given logical address A:
  Disk = A % disk_count
  Offset = A / disk_count

## Slide 17: Chunk Size
Disk 0 Disk 1 Disk 2 Disk 3
0 2 4 6
1 3 5 7
8 10 12 14
9 11 13 15
stripe
When are small chunks better?
When are large chunks better?
Notes: How to map given logical address with chunk size K?

## Slide 18: RAID-0: Analysis
What is capacity?
  N * C
How many disks can fail?
  0
Throughput?
  ?
Latency for one-op (read or write) performance
  T
Notes: Throughput: N*R, N*S

## Slide 19: RAID-0: Analysis
Performance: what is steady-state throughput for
  sequential reads
  sequential writes
  random reads
  random writes
  N * S
  N * S
  N * R
  N * R

## Slide 20: RAID-1: Mirroring
Keep two copies of all data.
Logical Blocks
Disk 0 Disk 1

## Slide 21: 4 disks
Disk 0 Disk 1 Disk 2 Disk 3
0 0 1 1
2 2 3 3
4 4 5 5
6 6 7 7
How many disks can fail?

## Slide 22: Assumptions
Assume disks are fail-stop.
  they work or they don’t
  we know when they don’t
Tougher Errors:
  latent sector errors
  silent data corruption

## Slide 23: RAID-1: Analysis
What is capacity?
  N / 2 * C
How many disks can fail?
  1 (or maybe N / 2)
Throughput?
  ???
Latency for one-op performance
  T for read, T+ for write

## Slide 24: RAID-1: Throughput
Performance: what is steady-state throughput for
  sequential reads
  sequential writes
  random reads
  random writes
  N/2 * S
  N/2 * S
  N * R
  N/2 * R

## Slide 25: Crashes
Operations: write (A) to 2
What if crash in between the writes to two disks?
Logical Blocks
Disk 0 Disk 1
  Consistent-update problem

## Slide 26: Consistent-update problem
Write-ahead log
Run recovery procedure upon a system failure
H/W Solution:
  Use non-volatile RAM in RAID controller.

## Slide 27: RAID-4 with 5 disks
Disk 0 Disk 1 Disk 2 Disk 3 Disk 4
0 1 2 3 PA0
4 5 6 7 PA1
8 9 10 11 PA2
12 13 14 15 PA3
How to calculate parity
  XOR is a good one
parity

## Slide 28: RAID-4: Analysis
What is capacity?
  (N-1) * C
How many disks can fail?
  1
Throughput?
  ???
Latency for one-op performance
  T for read, 2T+ for write

## Slide 29: RAID-4: Throughput
Performance: what is steady-state throughput for
  sequential reads
  sequential writes
  random reads
  random writes
    additive parity
    subtractive parity
  (N-1) * S
  (N-1) * S
  (N-1) * R
  R/2
  How to avoid parity bottleneck?

## Slide 30: RAID-5
Disk 0 Disk 1 Disk 2 Disk 3 Disk 4
0 1 2 3 PA0
5 6 7 PA1 4
10 11 PA2 8 9
15 PA3 12 13 14
PA4 16 17 18 19

## Slide 31: RAID-5: Analysis
What is capacity?
  (N-1) * C
How many disks can fail?
  1
Throughput?
  ???
Latency for one-op performance
  T for read, 2T+ for write

## Slide 32: RAID-5: Throughput
Performance: what is steady-state throughput for
  sequential reads
  sequential writes
  random reads
  random writes
  (N-1) * S
  (N-1) * S
  N * R
  N/4 * R

## Slide 33: All RAID
 | Reliability | Capacity
RAID-0 | 0 | N
RAID-1 | 1 | N / 2
RAID-4 | 1 | N - 1
RAID-5 | 1 | N - 1

## Slide 34: All RAID
 | Read Latency | Write Latency
RAID-0 | T | T
RAID-1 | T | T
RAID-4 | T | 2T
RAID-5 | T | 2T
RAID-5 can do more in parallel

## Slide 35: All RAID
 | Seq R | Seq W | Rand R | Rand W
RAID-0 | N*S | N*S | N*R | N*R
RAID-1 | N/2 * S | N/2 * S | N*R | N/2 * R
RAID-4 | (N-1)*S | (N-1)*S | (N-1)*R | R/2
RAID-5 | (N-1)*S | (N-1)*S | N*R | N/4 * R
RAID-5 is strictly better than RAID-4
RAID-0 is always fastest and has best capacity.
RAID-5 better than RAID-1 for sequential.
RAID-1 better than RAID-5 for random write.

## Slide 36: Next time
File systems, API